## Slide 1
1
1
15
Adapted from Miranda Baker, illustration by Natalie Renier
Water level and flow: schematic
hocean
h
h = hocean - h
water level
difference
Flow Q [m3/s]
(negative out of estuary)
water level decreases with time as water flows out of estuary
Moss Landing harbor
Moro Cojo Slough

## Slide 2
Rapid decreases in Moro Cojo water level during low tide in Monterey Bay
Spring-neap cycle, net inflow during periods of decreased tidal range every two weeks
Monterey and Moro Cojo water levels
Water level and flow: data

## Slide 3
Ocean water level higher
than Moro Cojo
Ocean water level lower
than Moro Cojo
[m]
flow, Q [m3/s]
weak flow into Moro Cojo when ocean water level is higher
Water level and flow
ADCP data from summer 2016
Tide gate closed  weak inflow when ocean water level is higher than Moro Cojo
Planned repairs for a 12”x12” adjustable opening to allow inflow
Theoretical inflow based on USDA water measurement manual
https://www.usbr.gov/tsc/techreferences/mands/wmm
Effect of future repairs on outflow?
inflow
ouflow
Theoretical flow through submerged 1 ft2 rectangular orifice
,
= 0.61

## Slide 4
Ocean water level higher
than Moro Cojo
Ocean water level lower
than Moro Cojo
inflow
outflow
Comparison before and after initial repairs
Initial repairs resulted in decreased inflow and outflow
These data are used to develop models of water level in Moro Cojo, forced by ocean water levels
Dashed lines are the equations used in the model
Scenario A – failed tide gates (based on red data points, 2015)
Scenario B – initial repairs
(based on blue data points, 2016)

## Slide 5
Comparing model scenarios for summer 2015 (before repairs)
If the model were perfect, the red and blue curves would look exactly the same (it is not perfect)
Model scenario B shows the effect that initial repairs would have had, if done immediately
Steady rise in sea level is associated with non-tidal ocean variability and occurs in both model scenarios
Model results: summer 2015

## Slide 6
Model results: historical data